GSOF-ArduBridge
### Arduino firmware installation:
The Arduino programming is done via the xloader application with a compiled version of the ArduBridgeFW firmware.
1. Open the xloader application
2. Select the COM port that the ArduinoUno R3 is connected to.
3. Select the FW Hex file you with to program (e.g., "IO_Bridge_V13.hex").
4. Press the "Upload" button and wait for the programming operation to finish (few seconds)
### Verify using RealTerm (Without Python):
Configure the port to 230400bps, 8bit, 1stop, no-parity and open it.
Send the value (0x1b)
Send the charecter '?' (0x3f)
The Arduino should reply with a message in the form of "GSOF Arduino Bridge 1.3"
### Verify using Python:
Follow the installation guide for the GSOF_ArduBridge python module.
### Few of the API specifications:
The below command are supported by the ArduBridge firmware:
Set a digital-pin direction: <'D'>,<pin#>,<val (0-Output, 1-Input>
Set a digital-pin state: <'O'>,<pin#>,<val (0/1)>
Read the state of a digital-pin: <'I'>,<pin#>,<val>
Set an analog-pin value: <'P'>,<pin#>,<val>
Read an analog-pin value: <'A'>,<pin#>,<val>
Read/Write from an SPI device: <'3'>,<DAT1>,<DAT2>…,<DATn>,<RST>
Write to I2C device: <'2'>,<'A'>,<DEV#>,<'L'>,<n+1>,<REG#>,<DAT1>, <DAT2>...<DATn>
Read from an I2C device: <'2'>,<'A'>,<DEV#>,<'L'>,<1>,<'w'>,<REG#>, <'2'>,<n>,<'R'>
note:'2' I2C packet header
     'w' write-restart
     'R' read
     'A' device-address
     'L' data length